## Slide 1: Mobile Unlock
Magnus Feuer
Jaguar Land Rover Open Software Technology Center

## Slide 2
Purpose
Use any smartphone
to unlock
any vehicle

## Slide 3
Overview
Key mgmt
website
Android unlock app
Unlock
Key management website [Cloud] Allow vehicle owners to provision and transmit keys to any android app
Android unlock app [Mobile Device] Runs a background service using keys to lock/unlock select vehicles
Unlock / Keyfob [Raspberry Pi] Receives, validates, and executes received lock/unlock command using a keyfob
Keyfob

## Slide 4
Use Case
Vehicle owner sends access rights to a mobile device
Mobile device receives and stores key
Subscriber walks up to vehicle
Mobile device uses Bluetooth to unlock vehicle

## Slide 5
A guest driver is provisioned with VIN and target Android device and google account
An RVI credential containing target service (jlr.com/[VIN]/unlock) is created and signed by the root certificate
RVI credential is transmitted from website to target Android device using Google Cloud Messaging
Unlock service on Android device receives credential and forwards it to the local RVI component
Key provisioning
Unlock service
Android
Website
Key Provisioning
XMPP
RVI
REST HTTP | JSON-RPC

## Slide 6
GPIO
RVI
Unlock service detects vehicle presence
Unlock service sends unlock command to Android RVI
RVI forwards command, with provisioned credentials, to Raspberry RVI using Bluetooth
Raspberry RVI validates command and forwards it to Unlock app
Unlock app manipulates GPIO pins to press the unlock button on keyfob
Vehicle
Android
Unlock App
RVI
Keyfob
Unlock Service
Raspberry Pi
iBeacon
bert-rpc/rfcomm

## Slide 7: Thank You
Magnus Feuer System Architect – Open Software Initiative
mfeuer@jaguarlandrover.com
+1-949-294 7871